| ENGINE ROOM | Check bilges, hoses for leaks |
| --- | --- |
|  | Check raw water seacock open |
|  | Check strainer |
|  | Check generator raw water seacock |
|  | Check generator strainer |
|  | Check fuel/water separator |
|  | Check coolant level |
|  | Check oil level engine |
|  | Check generator oil level |
|  | Check fuel valve alignments |
|  | Check battery water |
| ELECTRICAL | Check battery charge |
|  | Turn AC panel breakers off |
|  | Turn main AC panel breaker off |
|  | Disconnect shorepower cord at shore |
|  | Disconnect shorepower cord at boat |
|  | Turn on main DC breaker if not on |
|  | Turn on DC breakers for water, electronics, windlass (if anchored), refrigerator, head |
|  | Check bilge pumps on auto |
|  | Turn on VHF |
|  | Check steering range - center helm |
| INSTRUMENTS | Turn on plotter and radar |
|  | Verify set-ups on plotter and radar |
|  | Verify wheel center position |
| FUEL/WATER/HOLDING TANK | Verify fuel/holding tank/water levels OK |
| START-UP | Start engine |
|  | Observe volts, oil pressure, temp |
|  | Verify water flow at exhaust |
|  | Check transmission level |
|  | Turn on bow thruster |
|  | Verify closed - hatch, main cabin, head ports, side windows, rear door |
|  | Verify dinghy secured |
|  | Verify window blinds/curtains open |
| UNDOCKING | Undo all lines and secure inboard |
|  | Verify dinghy secured |
| WEIGHING ANCHOR | Pin or secure retrieved anchor |
| UNDERWAY | Stow fenders |
|  | Turn off bow thruster and windlass |
|  | Operate at required rpm range until stated minimum temp is reached. |
|  | Do not exceed rpm continuously |
|  | Do not run at _____ rpm for more than ____ minutes |
|  | Periodically check volts, pressure, temp |
|  | Periodically check shaft alley and engine room for leaks and unusual conditions |

12/31/10